## Slide 1: Algorithms and Data Structures for Logic Synthesis and Verification using Boolean Satisfiability
John Backes (back0145@umn.edu)
Advisor: Marc Riedel (mriedel@umn.edu)

## Slide 2: Work Since Prelim
Regression Verification Using Impact Summaries – Sub. to CAV 2013
  J. Backes, S. Person, N. Rungta, O. Tkachuk
Proteus: A Change Impact Analysis Framework
  J. Backes, S. Person, N. Rungta, O. Tkachuk
Ghost Talk: Mitigating EMI Signal Injection Attacks against Analog Sensors – Oakland 2013
  D. Kune, J. Backes, S. Clark, W. Xu, M. Reynolds, K. Fu, Y. Kim
Using Cubes of Non-state Variables With Property Directed Reachability – DATE 2013
  J. Backes, M. Riedel

## Slide 3: Overview of Topics

## Slide 4: Overview of Topics

## Slide 5: Overview of Topics

## Slide 6: Overview of Topics

## Slide 7: Overview of Topics

## Slide 8: Overview of Topics
1
2
3

## Slide 9: Theme: Synthesis + Verification

## Slide 10: Contributions
Cyclic Circuits
  SAT-Based Synthesis of Functions
  SAT-Based Analysis and Mapping
Resolution Proofs
  Reduction of Craig Interpolants
  Use as Synthesis Data Structure
Property Directed Reachability
  Extension to Non-state Variables

## Slide 11: Background

## Slide 12: Boolean Satisfiability
Is there some assignment of a, b, c, and d that satisfies this (CNF) formula?
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
“¬” or “x” is negation
“+” or “˅” is OR
“∙” or “˄” is AND
An appearance of a variable is a literal.
An OR of literals is a clause.

## Slide 13: Boolean Satisfiability
Is there some assignment of a, b, c, and d that satisfies this (CNF) formula?
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
“¬” or “x” is negation
“+” or “˅” is OR
“∙” or “˄” is AND
An appearance of a variable is a literal.
An OR of literals is a clause.

## Slide 14: Boolean Satisfiability
Is there some assignment of a, b, c, and d that satisfies this (CNF) formula?
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )
UNSAT!
“¬” or “x” is negation
“+” or “˅” is OR
“∙” or “˄” is AND
An appearance of a variable is a literal.
An OR of literals is a clause.

## Slide 15: Boolean Satisfiability
The Original NP-Complete Problem (Cook–Levin theorem)
  But can be very fast in practice
Used in Many Domains
  Artificial Intelligence
  Formal Verification
  Logic Synthesis

## Slide 16: Tseitin Transformation
Circuit can be converted into CNF formula in linear time (adding extra variables)

## Slide 17: Tseitin Transformation

## Slide 18: Tseitin Transformation

## Slide 19: Tseitin Transformation

## Slide 20: Tseitin Transformation

## Slide 21: Use Cubes of Non-state Variables with PDR

## Slide 22: Model Checking
What is model checking?
  Given a mathematical model of some real-world system, does the model exhibit a property?
  Models are transition systems (Finite state machines (FSMs))

## Slide 23: Example: Wallace Algorithm

## Slide 24: Example: Wallace Algorithm

## Slide 25: Example: Wallace Algorithm

## Slide 26: Example: Wallace Algorithm

## Slide 27: Example: Wallace Algorithm

## Slide 28: Example: Wallace Algorithm

## Slide 29: Example: Wallace Algorithm

## Slide 30: Example: Wallace Algorithm

## Slide 31: Wallace Properties
“Wallace never returns to his bed after leaving”
“Wallace will always eventually eat”
“Wallace never immediately eats after drinking”

## Slide 32: Symbolic Model Checking
Model checking suffers the “state-space explosion problem”
Algorithms use symbolic representation for sets of states
Original symbolic algorithms used BDDs more recent algorithms use SAT

## Slide 33: Model Checking Example
State graph is described by transition relation

## Slide 34: Model Checking Example
State graph is described by transition relation
  Primary Inputs
  State Inputs
  State Outputs
  Property Output

## Slide 35: Model Checking Example
Property holds for n transitions if ¬P is UNSAT in unrolled transition relation

## Slide 36: Model Checking Example
Property holds for n transitions if ¬P is UNSAT in unrolled transition relation

## Slide 37: Model Checking Example
Property holds for n transitions if ¬P is UNSAT in unrolled transition relation

## Slide 38: Model Checking Example
Property holds for n transitions if ¬P is UNSAT in unrolled transition relation

## Slide 39: Model Checking Example
Property holds for n transitions if ¬P is UNSAT in unrolled transition relation

## Slide 40: What is PDR?
Property Directed Reachability (PDR)
  New symbolic model checking algorithm
  Solves individual frames in isolation
Advantages over other algorithms
  SAT-Based not BDD-Based
  No need for long unrollings
  No spurious counter examples

## Slide 41: How does PDR work?
The trace contains sets of clauses Fi called frames.
Frame Fi symbolically represents over approximation of states reachable in i transitions.

## Slide 42: How Does PDR Work?
CNF formula: T 0
CNF formula: T 1
CNF formula: T 2

## Slide 43: How Does PDR Work?
SAT?: T 2 ˄ ¬P’
Result: x1x2x3x4
SAT?: T 1 ˄ x’1x’2x’3x’4
Result: x1x2x3x4
SAT?: I ˄ T 0 ˄ x’1x’2x’3x’4
Result: UNSAT!

## Slide 44: How Does PDR Work?
¬P
I
SAT?: Fi ˄ T ˄ ¬P’
SAT?: Fi-1 ˄ T ˄ x’1x’2x’3x’4
x1x2x3x4
F0
x1x2x3x4
x1x2x4
x1x2x3x4
Next State
Prev State
x1x2x3
x1x2x3x4
Cube Reduction!
Fi
CNF formula: T

## Slide 45: How to improve PDR
PDR requires small cubes to be effective
  Reductions via Ternary Valued Simulation
  Reductions via MUC inspection
Idea: The use of non-state variables may yield smaller cubes

## Slide 46: Intuition for Non-State Variables
Fi-1
Fi
Three cubes in terms of x0x1x2x3 blocked by one cube in terms of g0g1!

## Slide 47: Shifting the Transition Relation
Fi-1
Fi

## Slide 48: Shifting the Transition Relation
Fi-1
Fi

## Slide 49: Shifting the Transition Relation
Fi-1
Fi

## Slide 50: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
┴
“ ” is an
unknown value

## Slide 51: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
┴
“ ” is an
unknown value

## Slide 52: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
┴
“ ” is an
unknown value

## Slide 53: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
┴
“ ” is an
unknown value

## Slide 54: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
┴
“ ” is an
unknown value

## Slide 55: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
┴
“ ” is an
unknown value

## Slide 56: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
┴
“ ” is an
unknown value

## Slide 57: Ternary Valued Simulation
After solving Query: Fi ˄ T ˄ x’6x’7
  Satisfying assignment: x1x2x3x4
  Cube reduced: x1x3x4
┴
“ ” is an
unknown value

## Slide 58: Ternary Sim with Gate Vars
Slightly more complex because of variable dependence
Algorithm:
  Order variables ascending by logic level
  If the variables value is determined by fanins: remove it
  Otherwise try setting to:
┴

## Slide 59: Ternary Gate Vars Example
After solving Query: Fi ˄ T ˄ m’0m’1m’2
  Satisfying assignment: g0g1g2

## Slide 60: Ternary Gate Vars Example
After solving Query: Fi ˄ T ˄ m’0m’1m’2
  Satisfying assignment: g0g1g2

## Slide 61: Ternary Gate Vars Example
After solving Query: Fi ˄ T ˄ m’0m’1m’2
  Satisfying assignment: g0g1g2

## Slide 62: Ternary Gate Vars Example
After solving Query: Fi ˄ T ˄ m’0m’1m’2
  Satisfying assignment: g0g1g2

## Slide 63: Ternary Gate Vars Example
After solving Query: Fi ˄ T ˄ m’0m’1m’2
  Satisfying assignment: g0g1g2
  Reduced Cube: g0g1
Value Determined
by inputs!

## Slide 64: Experimental Setup
Ternary sim run twice: only gate vars and only state vars
Vars are removed from cube by logic level and by priority
After both passes the smaller cube is chosen

## Slide 65: SAT Results

## Slide 66: UNSAT Results
…
…
…
…
…
…
…
…

## Slide 67: Discussion
Extension seems to work well for satisfiable benchmarks
Does not seem to work as well for unsatisfiable benchmarks
Randomness also affects the results.

## Slide 68: Other Things We Tried
Probabilistically chose gate variables
Used simulated annealing type approach that gradually changed from gate cubes to state cubes
Placed limits on max height of logic level used

## Slide 69: Synthesizing Cyclic Dependencies with Craig Interpolation

## Slide 70: Craig Interpolation
Given formulas A and B such that A → ¬B, there exists I such that A → I → ¬B
  I only contains variables that are present in both A and B.
A
I
B

## Slide 71: Craig Interpolation Cont.
For an instance of unsatisfiablity, if the clauses are divided into sets A and B then A → ¬B.
  An interpolant I can be generated from a proof of unsatisfiability of A and B.
  The structure of this proof influences the structure of I

## Slide 72: Generating I Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )

## Slide 73: Generating I Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )

## Slide 74: Generating I Example
(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)
(
c
) (
¬
c
)
( )

## Slide 75: Generating I Example
(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)
(
c
) (
¬
c
)
( )
a c ¬a c

## Slide 76: Generating I Example
)(
¬
d
)
(
d
+
¬c
)
(
c
) (
¬
c
)
( )
a c ¬a c

## Slide 77: Generating I Example
(
¬
d
)
(
c
) (
¬
c
)
( )
a c ¬a c

## Slide 78: Generating I Example
a c ¬a c
¬d
( )
(
¬
d
)

## Slide 79: Generating I Example
a c ¬a c
¬d
I(a,c)
A
I
B

## Slide 80: Applications
Model Checking1
  Interpolants are used to over approximate the set of reachable states in a transition relation.
Functional Dependencies2
  Interpolants are used to generate a dependency function in terms of a specified support set.
  The size of the interpolant directly correlates to the size of the circuit implementation.
1(K. L. McMillan. Interpolation and SAT-based model checking. ICCAV, 2003.)
2C.-C. Lee, J.-H. R. Jiang, C.-Y. Huang, and A. Mishchenko. Scalable exploration of functional dependency by interpolation and incremental SAT solving. ICCAD, 2007.

## Slide 81
Cyclic Circuit: 2 functions, 5 variables, 2 fan-in 4 gates.
a
b
c
c
d
e
Acyclic Circuit: at least 3 fan-in 4 gates.
Cyclic Combinational Circuits

## Slide 82: How can one make a cyclic circuit?
Consider some acyclic circuit
Pick support variables
Pick target support sets in a cyclic fashion

## Slide 83: What is wrong with the old approach?
Old method uses BDDs.
  These do not scale well with circuit size.
Old method for functional dependencies relies on algebraic manipulation.
  Also does not scale well with circuit size.

## Slide 84: What is better with the new approach
Uses SAT-based method for functional dependency.
SAT-based cyclic analysis during synthesis.
  This scales better for larger circuits.

## Slide 85: Functional Dependency
a | b | c | f0 | f1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
Two functions of three variables.
For every assignment of f0 and c, there is a unique value for f1.
This is necessary and sufficient to express f1 in terms of f0 and c.

## Slide 86: Functional Dependency
a | b | c | f0 | f1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
Two functions of three variables.
For every assignment of f0 and c, there is a unique value for f1.
This is necessary and sufficient to express f1 in terms of f0 and c.

## Slide 87: Functional Dependency
a | b | c | f0 | f1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
Two functions of three variables.
For every assignment of f0 and c, there is a unique value for f1.
This is necessary and sufficient to express f1 in terms of f0 and c.

## Slide 88: Functional Dependency
a | b | c | f0 | f1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
Two functions of three variables.
For every assignment of f0 and c, there is a unique value for f1.
This is necessary and sufficient to express f1 in terms of f0 and c.

## Slide 89: Functional Dependency
a | b | c | f0 | f1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
Two functions of three variables.
For every assignment of f0 and c, there is a unique value for f1.
This is necessary and sufficient to express f1 in terms of f0 and c.

## Slide 90: Functional Dependency
Two functions of three variables.
For every assignment of f0 and c, there is a unique value for f1.
This is necessary and sufficient to express f1 in terms of f0 and c.
a | b | c | f0 | f1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 0
c | f0 | f1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 91: Functional Dependency
C.-C. Lee, J.-H. R. Jiang, C.-Y. Huang, and A. Mishchenko, “Scalable exploration of functional dependency by interpolation and incremental SAT solving”, ICCAD ‘07
If SAT, the dependency function h does not exist.
If UNSAT, Craig Interpolation can be used to derive an expression for h.
Tells us if f0 (x0, x1, … , xn) can be expressed in terms of some function h (f0, f1, f2, f3)

## Slide 92: Cyclic Dependency
A cyclic dependency is combinational if for every assignment of primary input variables, every function has a definite value.
a | b | f1 | f0
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a | c | f0 | f1
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 93: Cyclic Dependency
A cyclic dependency is combinational if for every assignment of primary input variables, every function has a definite value.
a | b | f1 | f0
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a | c | f0 | f1
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
a=b=0 controls f0
a=c=1 controls f1

## Slide 94: Cyclic Dependency
A cyclic dependency is combinational if for every assignment of primary input variables, every function has a definite value.
a | b | f1 | f0
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a | c | f0 | f1
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
a=c=0, b=1 controls neither!

## Slide 95: Cyclic Dependency
The circuit is not combinational if three conditions are satisfied
  All primary input variables the same in each row.
  Controlling values are propagated.
  Some function is toggling.
a | b | f1 | f0
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a | c | f0 | f1
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
a=c=0, b=1 controls neither!

## Slide 96: Cyclic Dependency
Create a SAT instance that satisfies three conditions.
A Left and a Right copy of each dependency function.
  Each copy considers one row of the truth table.

## Slide 97: Synthesizing Cyclic Dependencies
Select a candidate set of target functions and support sets.
Generate their implementations via Craig Interpolation.
Use branch and bound search to pick solution.
Use SAT to verify if solution is combinational.

## Slide 112: What are the problems with the new approach?
The structure of the interpolants is relatively poor.
Because of this, we use support set size as our cost function.
  This can be a valid metric for FPGAs.

## Slide 113: Reduction of Interpolants For Logic Synthesis

## Slide 114: Generating I Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )
a c ¬a c
¬d

## Slide 115: Generating I Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
d
+
¬c
)
( )
(
¬
c
)
(
c
)

## Slide 116: Generating I Example
>

## Slide 117: Draw Backs
Model Checking
  Interpolants that are large over approximations can trigger false state reachability.
Functional Dependencies
  In many cases the structure of the interpolant may be very redundant and large.

## Slide 118: Proposed Solution
Goal: reduce size of an interpolant generated from a resolution proof.
  Change the structure of a proof with the aim of reducing interpolant size.
  In general, the fewer intermediate nodes in the proof, the smaller then interpolant.

## Slide 119: Resolution Proofs
A proof of unsatisfiability for an in instance of SAT forms a graph structure.
The original clauses are called the roots and the empty clause is the only leaf.
Every node in the graph (besides the roots) is formed via Boolean resolution.
  I.e.: (c + d)(¬c + e) → (d + e)
  Here “c” is referred to as the pivot variable.

## Slide 120: Generating Interpolants
Interpolants are generated by calling a recursive function on the empty clause.
Logic gates are created on the intermediate nodes.
  The function of the gate depends on which set of root nodes the pivot variable is present in.
The procedure terminates on root nodes.

## Slide 121: Proposition 1
Nodes resolved only from A (or B) can be considered as roots of A (or B).
Proof: Given clauses C, D, and E such that (C)(D) → (E), (C)(D) ≡ (C)(D)(E).
A
I
B

## Slide 122: Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )

## Slide 123: Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )

## Slide 124: Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
d
+
¬c
)
( )
(
¬
c
)
(
c
)

## Slide 125: Example
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
d
+
¬c
)
( )
(
¬
c
)
(
c
)
0

## Slide 126: Observation
Proofs with few resolutions between clauses of A and B will tend to have smaller interpolants.
  We refer to nodes that have ancestors for A and B as mixed nodes.
  We refer to proofs with few mixed nodes as being more disjoint.
Our goal: find a more disjoint proof before generating the interpolant.

## Slide 127: Proposition 2
If node c in a proof is implied by root nodes R, then all assignments that satisfy the clauses of R also satisfy c
Proof: since R → c, whenever R = 1, c = 1

## Slide 128: SAT Based Methods
Since R → c the SAT instance (R)(¬c) will be unsatisfiable.
R. Gershman used this observation to find Minimum Unsatisfiable Cores (MUCs) for resolution proofs1.
1R. Gershman, M. Koifman, and O. Strichman. An approach for extracting a small unsatisfiable core. Formal Methods in System Design, 2008.

## Slide 129: Example
What if we want to know if (¬c) can be implied by A?
Check the satisfiability of:
(a + ¬c + d)(¬a + ¬c + d)(a+ c)(¬a + c)(¬d)(c)
Root of A?
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )
=
UNSAT!

## Slide 130: Example
What if we want to know if ( ) can be implied by A?
Check the satisfiability of:
(a + ¬c + d)(¬a + ¬c + d)(a+ c)(¬a + c)(¬d)
Root of A?
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )
=
UNSAT!

## Slide 131: Example
What if we want to know if ( ) can be implied by A?
Check the satisfiability of:
(a + ¬c + d)(¬a + ¬c + d)(a+ c)(¬a + c)(¬d)
Root of A?
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )
=
UNSAT!

## Slide 132: Proposed Method

## Slide 133: Optimizations
The complexity of this approach is dominated by solving different SAT instances.
We can reduce the number of calls to the SAT solver by checking mixed nodes in specific orders.

## Slide 134: Optimization 1
If node 1 is a root of A (B) then we don’t need to check node 3.
...( )( )( )( )
( )( )( )...
(
3
) (
4
) (
5
)
(
1
) (
2
)
( )
……
..

## Slide 135: Optimization 1
If node 1 is a root of A (B) then we don’t need to check node 3.
...( )( )( )( )
( )( )( )...
(
3
) (
4
) (
5
)
(
1
) (
2
)
( )
……
..

## Slide 136: Optimization 1
If nodes 1 and 2 are roots of A (B) then we don’t need to check nodes 3 4 or 5.
...( )( )( )( )
( )( )( )...
(
3
) (
4
) (
5
)
(
1
) (
2
)
( )
……
..

## Slide 137: Optimization 1
If nodes 1 and 2 are roots of A (B) then we don’t need to check nodes 3 4 or 5.
...( )( )( )( )
( )( )( )...
(
3
) (
4
) (
5
)
(
1
) (
2
)
( )
……
..
Checking nodes near the leaf first is a backward search

## Slide 138: Optimization 2
If nodes and 3 and 4 are roots of A (B) then node 1 can be considered a root of A (B)
...( )( )( )( )
( )( )( )...
(
3
) (
4
) (
5
)
(
1
) (
2
)
( )
……
..

## Slide 139: Optimization 2
If nodes and 3 and 4 are roots of A (B) then node 1 can be considered a root of A (B)
...( )( )( )( )
( )( )( )...
(
3
) (
4
) (
5
)
(
1
) (
2
)
( )
……
..

## Slide 140: Optimization 2
If nodes and 3 and 4 are roots of A (B) then node 1 can be considered a root of A (B)
...( )( )( )( )
( )( )( )...
(
3
) (
4
) (
5
)
(
1
) (
2
)
( )
……
..
Checking nodes near the roots first is a forward search

## Slide 141: Forward vs. Backward Search
Backward Search
  Eliminates many mixed nodes at once
  May take many SAT checks before we prove a node to be a root.
Forward Search
  Nodes toward the beginning are more likely to be roots
  May require more checks then backward search.

## Slide 142: Incremental Techniques
Each call to the SAT solver is very similar.
  Each instance is in the form (A)(¬c) or (B)(¬c).
The negated literals of clause c can be set as unit assumptions to the SAT Solver.
  We then just solve the same instance repeatedly with different assumptions.
Variables aoff and boff can be added to the clauses of A and B respectively.

## Slide 143: Example
What if we want to know if (d + ¬c) can be implied by A?
Assume aoff = 0, boff = 1, d = 0, and c = 1. Then check the satisfiability of:
(a + ¬c + d + aoff)(¬a + ¬c + d + aoff)(a+ c + aoff)(¬a + c + aoff) (¬d + aoff)(d + ¬c + boff)(a + b + boff)
Root of A?
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )
= UNSAT!

## Slide 144: Experiment
Searched for different functional dependencies in benchmark circuits.
  Found small support sets for POs expressed in terms of other POs and PIs.
Performed forward and backward search on the resolution proofs.
  The number of SAT checks was limited to 2500.
  This limit was reached for the larger proofs.

## Slide 145: Experiment Cont.
After the new interpolants from the modified resolution proofs are. generated, the size is compared to the un modified proofs.
The size after running logic minimization on the modified and non modified interpolants is also compared.

## Slide 146: Results (table3 benchmark)
table3 Benchmark: Forward Search |  |  |  |  |  |  |  |  | 
Function | # Nodes | Orig Size | New Size | Checked | Found | Time (s) | Orig Reduced | New Reduced | Ratio
0 | 32262 | 277 | 267 | 2500 | 61 | 80.85 | 105 | 93 | 0.89
1 | 128654 | 1254 | 1254 | 2500 | 0 | 281.31 | 328 | 329 | 1.00
2 | 95042 | 638 | 630 | 2500 | 283 | 218.25 | 248 | 226 | 0.91
3 | 71647 | 682 | 648 | 2500 | 423 | 157.66 | 273 | 215 | 0.79
4 | 57015 | 776 | 743 | 2500 | 432 | 126.26 | 380 | 364 | 0.96
5 | 47285 | 657 | 657 | 2500 | 0 | 106.23 | 251 | 233 | 0.93
6 | 43884 | 268 | 245 | 2500 | 578 | 94.67 | 91 | 104 | 1.14
7 | 26714 | 287 | 271 | 2500 | 335 | 64.37 | 144 | 126 | 0.88
8 | 31715 | 116 | 90 | 2500 | 48 | 79.4 | 55 | 34 | 0.62
9 | 13182 | 43 | 36 | 1090 | 65 | 17.25 | 22 | 18 | 0.82
10 | 70964 | 867 | 850 | 2500 | 576 | 146.85 | 413 | 397 | 0.96
11 | 31772 | 253 | 229 | 2500 | 67 | 80.12 | 86 | 107 | 1.24
12 | 45784 | 376 | 360 | 2500 | 404 | 98.61 | 172 | 184 | 1.07
13 | 29078 | 408 | 373 | 2500 | 757 | 64.73 | 130 | 55 | 0.42

## Slide 147: Results (table3 benchmark)
table3 Benchmark: Backward Search |  |  |  |  |  |  |  |  | 
Function | Nodes | Orig Size | New Size | Checked | Found | Time (s) | Orig Reduced | New Reduced | Ratio
0 | 32262 | 277 | 129 | 2500 | 20 | 85.88 | 105 | 58 | 0.55
1 | 128654 | 1254 | 1238 | 2500 | 5 | 287.62 | 328 | 346 | 1.05
2 | 95042 | 638 | 574 | 2500 | 8 | 225.37 | 248 | 217 | 0.88
3 | 71647 | 682 | 469 | 2500 | 45 | 179.96 | 273 | 177 | 0.65
4 | 57015 | 776 | 490 | 2500 | 26 | 144.83 | 380 | 193 | 0.51
5 | 47285 | 657 | 611 | 2500 | 8 | 114.33 | 251 | 242 | 0.96
6 | 43884 | 268 | 224 | 2500 | 8 | 107.96 | 91 | 106 | 1.16
7 | 26714 | 287 | 87 | 2500 | 27 | 76.61 | 144 | 51 | 0.35
8 | 31715 | 116 | 76 | 2500 | 15 | 85.23 | 55 | 34 | 0.62
9 | 13182 | 43 | 36 | 1017 | 3 | 16.55 | 22 | 18 | 0.82
10 | 70964 | 867 | 349 | 2500 | 41 | 179.22 | 413 | 192 | 0.46
11 | 31772 | 253 | 191 | 2500 | 8 | 82.38 | 86 | 50 | 0.58
12 | 45784 | 376 | 203 | 2500 | 34 | 120 | 172 | 117 | 0.68
13 | 29078 | 408 | 112 | 2500 | 32 | 84.29 | 130 | 37 | 0.28

## Slide 148: Results (Summarized)
Forward Search |  |  |  |  |  | 
Benchmark | Nodes | Checked | Found | % Change | % Change Reduced | Time (s)
apex1 | 28279 | 2413 | 30 | -4.89% | -2.73% | 69.48
apex3 | 68585 | 1494 | 21 | -2.12% | -1.47% | 140.99
styr | 9373 | 2143 | 88 | -8.71% | -5.71% | 18.3
s1488 | 5748 | 824 | 29 | -9.24% | -8.41% | 7.62
s1494 | 10488 | 1266 | 21 | -6.69% | -4.43% | 15.51
s641 | 46416 | 1886 | 39 | -26.67% | -2.33% | 97.45
s713 | 42412 | 1910 | 89 | -36.00% | -3.70% | 89.16
table5 | 35373 | 2500 | 252 | -13.83% | -4.08% | 48.05
vda | 12951 | 2011 | 120 | -18.78% | -17.33% | 27.34
sbc | 13951 | 1094 | 8 | -1.46% | -1.08% | 19.09

## Slide 149: Results (Summarized)
Backward Search |  |  |  |  |  | 
Benchmark | Nodes | Checked | Found | % Change | % Change Reduced | Time (s)
apex1 | 28279 | 2384 | 6 | -8.95% | -5.84% | 72.03
apex3 | 68585 | 1485 | 5 | -8.41% | -5.24% | 145.63
styr | 9373 | 2124 | 10 | -11.57% | -10.14% | 19.36
s1488 | 5748 | 797 | 5 | -9.92% | -9.59% | 7.98
s1494 | 10488 | 1241 | 7 | -6.93% | -5.19% | 15.83
s641 | 46416 | 1820 | 14 | -42.22% | -2.78% | 95.37
s713 | 42412 | 1724 | 17 | -43.90% | -6.20% | 82.86
table5 | 35373 | 2358 | 7 | -26.67% | -15.83% | 81.16
vda | 12951 | 1850 | 7 | -21.72% | -19.72% | 27.07
sbc | 13951 | 1087 | 1 | -1.46% | -0.92% | 19.09

## Slide 150: Summary of Thesis

## Slide 151: The Analysis of Cyclic Circuits with Boolean Satisfiability (ICCAD08)
SAT-based algorithm for analyzing cyclic circuits on the gate level.
Also work discussing mapping of cyclic circuits.

## Slide 152
1
1
The Analysis of Cyclic Circuits with Boolean Satisfiability (ICCAD08)

## Slide 153: The Analysis of Cyclic Circuits with Boolean Satisfiability (ICCAD08)

## Slide 154: The Synthesis of Cyclic Dependencies with Craig Interpolation (IWLS09, TODAES12)
Used SAT for functional level analysis
Craig Interpolation to generate the dependencies
Branch and bound to find different solutions

## Slide 155
Consider some acyclic circuit
Pick support variables
Pick target support sets in a cyclic fashion
The Synthesis of Cyclic Dependencies with Craig Interpolation (IWLS09, TODAES12)

## Slide 156: Reduction of Interpolants For Logic Synthesis (ICCAD10)
Restructured resolution proofs to make smaller interpolants
Used incremental SAT techniques to increase performance

## Slide 157: Reduction of Interpolants For Logic Synthesis (ICCAD10)
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
c
) (
¬
c
)
( )
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
d
+
¬c
)
( )
(
¬
c
)
(
c
)
(
a
+
¬
c
+
d
)(
¬
a
+
¬
c
+
d
)(
a
+
c
)(
¬
a
+
c
)(
¬
d
)
(
d
+
¬c
)(
a
+
b
)
(
d
+
¬c
)
( )
(
¬
c
)
(
c
)
0

## Slide 158: Resolution Proofs as a Data Structure For Logic Synthesis (IWLS11)
Advocated using resolution proofs to perform large restructurings
Showed that many nodes can be shared among similar proofs

## Slide 159: Resolution Proofs as a Data Structure For Logic Synthesis (IWLS11)
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 160: Resolution Proofs as a Data Structure For Logic Synthesis (IWLS11)
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 161: Resolution Proofs as a Data Structure For Logic Synthesis (IWLS11)
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 162: Resolution Proofs as a Data Structure For Logic Synthesis (IWLS11)
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 163: PDR and Gate Variables (DATE13)
Extended PDR algorithm to use cubes of non-state variables
Improved performance for satisfiable benchmarks

## Slide 164: PDR and Gate Variables (DATE13)
Fi-1
Fi

## Slide 165
PI Vars
State Vars
Gate Vars
Next State Vars
PDR and Gate Variables (DATE13)

## Slide 166
PI Vars
Next Gate Vars
Gate Vars
PDR and Gate Variables (DATE13)

## Slide 167: Future Directions

## Slide 168: Cyclic Re-Writing
DAG-Aware AIG Re-Writing is powerful for acyclic circuits
  Uses pre-computed functions
  Computes feasible cuts of the circuit
Can re-writing be performed with cyclic circuits?

## Slide 169: Cyclic Re-Writing Challenges
After each cut is replaced combinational analysis must be performed
  We can use SAT-Based analysis!
Re-writing would require a database of good cyclic functions
  Cyclic circuits implementing a single function?

## Slide 170: Single Output Cyclic Circuits
Do there exists small cyclic circuits implementing a single function?

## Slide 171: Single Output Cyclic Circuits
Do there exists small cyclic circuits implementing a single function?

## Slide 172: Resolution Proofs and Interpolants
Techniques may be extended to improve abstractions (over-approximations)
Methods for generating good initial proofs (rather than quickly solving instances)

## Slide 173: Property Directed Reachability
The algorithm is very young
New heuristics for cube minimization
Possible extensions to probabilistic model checking

## Slide 174: Future Plans

## Slide 175: Resolution Proofs as a Universal Data Structure for Logic Synthesis

## Slide 176: Data Structures
Sum of Products (SOPs)
  Advantages: explicit, readily mapable.
  Disadvantages: not scalable.
Binary Decision Diagrams (BDDs)
  Advantages: canonical, easily manipulated.
  Disadvantages: not readily mapable, not scalable.

## Slide 177: Data Structures
And Inverter Graphs (AIGs)
  Advantages:
    Compact.
    Easily convertible to CNFs.
    Scalable, efficient.
  Disadvantages:
    Hard to perform large structural changes.

## Slide 178: Resolution Proofs
Implicitly extracted from SAT solvers; converted to logic via Craig Interpolation.
Utilize as a data structure to perform logic manipulations.
Advantages:
  Scalable, efficient.
  Can effect large structural changes.

## Slide 179: AIG Synthesis
Re-writing
  Cuts are replaced by pre-computed optimal structures (Mishchenko ’06).
SAT Sweeping
  Nodes of an AIG can be merged by proven equivalence (Zhu ‘06).
SAT-Based Resubstitution
  Target nodes are recomputed from other nodes (Lee ‘07).

## Slide 180: AIG Synthesis
SAT-Sweeping (merging equivalent nodes)

## Slide 181: AIG Synthesis
SAT-Sweeping (merging equivalent nodes)

## Slide 182: AIG Synthesis
AIG re-writing
  Local manipulations performed on windows
  Local minimums can be reached

## Slide 183: AIG Synthesis
AIG re-writing
  Local manipulations performed on windows
  Local minimums can be reached

## Slide 184: AIG Synthesis
AIG re-writing
  Local manipulations performed on windows
  Local minimums can be reached

## Slide 185: Resubstitution a.k.a. Functional Dependencies
Given target:
f (z1,z2,…,zn),
Given candidates: x1(z1,z2,…,zn), x2(z1,z2,…,zn), …, xm(z1,z2,…,zn)
is it possible to implement f (x1,x2,…,xm)?

## Slide 186: Aig Synthesis
Resubstitution
  f (x1,x2)?

## Slide 187: Aig Synthesis
Resubstitution
  f (x1,x2)?
  Large changes
  This question is formulated as a SAT instance.
  Craig Interpolation provides implementation.

## Slide 188: Generating Multiple Dependencies
Often, goal is to synthesize dependencies for multiple functions with overlapping support sets.
In this case, multiple proofs are generated and then interpolated.

## Slide 189: Example
Large portions of a network can be converted to a resolution proof.
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 190: Example
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 191: Example
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 192: Observation
There are often many ways to prove a SAT instance unsatisfiable.
Same/similar nodes shared between different proofs.

## Slide 193: Example
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 194: Example
fj (x1,x2,x3,x4,x5,x6)?
fk (x1,x2,x3,x4,x5,x6)?

## Slide 195: Restructuring Mechanism
Some clause c can be resolved from some set of clauses W iff (W)(c) is unsatisfiable.
The resolution proof of (W)(c) can be altered to show how c can be resolved from W.
(Gershman ‘08)

## Slide 196: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 197: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 198: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 199: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 200: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 201: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 202: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 203: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 204: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 205: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 206: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 207: Example
Can (a + b) be resolved from (a + e + d)(a + b + d) (a + b + d + e)?
(Gershman ‘08)

## Slide 208: Proposed method
Select potential target functions with the same support set:
  f1(x1,x2,…,xm), f2(x1,x2,…,xm), … , fn(x1,x2,…,xm)
Generate collective resolution proof.
Structure the proofs so that there are more shared nodes.

## Slide 209: Which nodes can be shared?
For the interpolants to be valid:
  The clause partitions A and B must remain the same.
  The global variables must remain the same.

## Slide 210: Which nodes can be shared?
( f )(CNFLeft)( f *)(CNFRight)(x1 = x1*)(x2 = x2*)…(xm = xm*)
A
B
f (x1,x2,…,xm):
( g)(CNFLeft)( g *)(CNFRight)(x1 = x1*)(x2 = x2*)…(xm = xm*)
A
B
g (x1,x2,…,xm):

## Slide 211: Which nodes can be shared?
( f )(CNFLeft)( f *)(CNFRight)(x1 = x1*)(x2 = x2*)…(xm = xm*)
A
B
f (x1,x2,…,xm):
( g)(CNFLeft)( g *)(CNFRight)(x1 = x1*)(x2 = x2*)…(xm = xm*)
A
B
g (x1,x2,…,xm):
Only the assertion clauses differ

## Slide 212: Restructuring Proofs
Color the assertion clauses and descendants black.
Color the remaining clauses white.
Resolve black nodes from white nodes.

## Slide 213: Restructuring Proofs

## Slide 214: Restructuring Proofs

## Slide 215: Restructuring Proofs

## Slide 216: Proposition
The interpolants from restructured proofs are equivalent.
Proof:
The roots of all white clauses are present in the original SAT instance.
The global variables are the same for each SAT instance.

## Slide 217: Experiment
Test to see to what extent proofs can be restructured.
  How many black nodes can be resolved from white nodes?
Generated resolution proofs from benchmark circuits.
  POs specified in terms of all PIs.

## Slide 218
Benchmark | Orig. Num. White | Orig. Num. Black | Num. Checked | Num. Sharable | % Sharable | Time (s)
dk15 | 1743 | 581 | 581 | 175 | 30.12 | 0.04
5xp1 | 3203 | 1636 | 1636 | 275 | 16.81 | 0.18
sse | 3848 | 2650 | 2650 | 563 | 21.25 | 0.28
ex6 | 4055 | 2731 | 2731 | 588 | 21.53 | 0.29
s641 | 6002 | 5148 | 5148 | 2269 | 44.08 | 0.46
s510 | 7851 | 5092 | 5092 | 1155 | 22.68 | 0.74
s832 | 15359 | 14826 | 14826 | 3358 | 22.65 | 3.67
planet | 40516 | 43387 | 43387 | 10640 | 24.52 | 26.39
styr | 44079 | 54128 | 54128 | 16578 | 30.63 | 33.88
s953 | 49642 | 46239 | 46239 | 12252 | 26.5 | 31.99
bcd | 96385 | 109167 | 103514 | 34349 | 33.18 | 200
table5 | 137607 | 288461 | 69070 | 27848 | 40.32 | 200
table3 | 177410 | 283066 | 47279 | 24454 | 51.72 | 200

## Slide 219: Discussion
Can effect large structural changes.

## Slide 220: Discussion
Preliminary results show that there is significant potential for node sharing.
Techniques are highly scalable.
  Calls to SAT solver are incremental.
  Heuristics could improve scalability.

## Slide 221: How does PDR work?
The trace contains sets of clauses Fi called frames.
Frame Fi symbolically represents over approximation of states reachable in i transitions.

## Slide 222: Trace Properties
The 0th frame is initial states ( F0 = I )
Each frame implies the next ( Fi → Fi+1 )
Next states are reachable in one transition from current ( Fi ˄ T→ F’i+1 )
Every frame satisfies the property; except the last ( Fi → P , i ≠ n)

## Slide 223: Algorithm Outline
Consists of two phases:
  The blocking phase: determines if cube S can be blocked in previous time frame i-1 by solving: Fi-1 ˄ T ˄ S’
  The propagation phase: determines if cube S can be blocked in next time frame i+1 by solving: Fi ˄ T ˄ S’

## Slide 224: PDR Example
F0 = I
F1
F1 ˄ T ˄ ¬P
Query:
(¬x1˅¬x2˅¬x3)
¬P
I
F0 ˄ T ˄ x’1x’2x’3x’4
SAT!
UNSAT!
x1x2x3x4
*Blocking Phase*
x4 not in proof!

## Slide 225: PDR Example
F0 = I
F1
F1 ˄ T ˄ ¬P
Query:
¬P
I
F0 ˄ T ˄ x’1x’3x’4
SAT!
UNSAT!
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
x1x3x4
*Blocking Phase*

## Slide 226: PDR Example
F0 = I
F1
F1 ˄ T ˄ ¬P
Query:
(¬x1˅¬x5)
¬P
I
F0 ˄ T ˄ x’1x’5
SAT!
UNSAT!
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
x1x5
*Blocking Phase*

## Slide 227: PDR Example
F0 = I
F1
F1 ˄ T ˄ ¬P
Query:
¬P
I
UNSAT!
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
*Blocking Phase*

## Slide 228: PDR Example
F0 = I
F1
Query:
¬P
I
F2
F1 ˄ T ˄ x’1x’2x’3
*Propagation Phase*
UNSAT!
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)

## Slide 229: PDR Example
F0 = I
F1
Query:
¬P
I
F2
F1 ˄ T ˄ x’1x’3x’4
*Propagation Phase*
SAT!
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)

## Slide 230: PDR Example
F0 = I
F1
Query:
¬P
I
F2
F1 ˄ T ˄ x’1x’5
*Propagation Phase*
SAT!
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)

## Slide 231: PDR Example
F0 = I
F1
Query:
¬P
I
F2
F2 ˄ T ˄ ¬P
SAT!
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)
x1x3x4
F1 ˄ T ˄ x’1x’3x’4
x6x7
SAT!
*Blocking Phase*

## Slide 232: PDR Example
F0 = I
F1
Query:
¬P
I
F2
SAT!
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)
F1 ˄ T ˄ x’1x’3x’4
x6x7x8
F0 ˄ T ˄ x’6x’7x’8
UNSAT!
(¬x6˅¬x7)
*Blocking Phase*
x8 not in proof!

## Slide 233: PDR Example
F0 = I
F1
Query:
¬P
I
F2
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)
F0 ˄ T ˄ x’6x’7
UNSAT!
(¬x6˅¬x7)
F1 ˄ T ˄ x’1x’3x’4
(¬x1˅¬x3˅¬x4)
*Blocking Phase*

## Slide 234: PDR Example
F0 = I
F1
Query:
¬P
I
F2
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)
SAT!
(¬x6˅¬x7)
F2 ˄ T ˄ ¬P
(¬x1˅¬x3˅¬x4)
x1x5
F1 ˄ T ˄ x’1x’5
UNSAT!
(¬x1˅¬x5)
*Blocking Phase*

## Slide 235: PDR Example
F0 = I
F1
Query:
¬P
I
F2
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)
(¬x6˅¬x7)
F2 ˄ T ˄ ¬P
(¬x1˅¬x3˅¬x4)
UNSAT!
(¬x1˅¬x5)
*Blocking Phase*

## Slide 236: PDR Example
F0 = I
F1
Query:
¬P
I
F2
(¬x1˅¬x5)
(¬x1˅¬x2˅¬x3)
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x2˅¬x3)
(¬x6˅¬x7)
F1 ˄ T ˄ x’6x’7
(¬x1˅¬x3˅¬x4)
(¬x1˅¬x5)
*Propagation Phase*
UNSAT!
(¬x6˅¬x7)
F1 = F2 , Fn → P